DESCRIPTION

This work shall consist of furnishing and installing Sign Post and Sign Post Base in soil as shown on the MCDOT standard details and to the satisfaction of the engineer.

MATERIAL

The post shall be 2” square perforated galvanized tube 12’-0” long.  The post base shall be 2 ¼” square perforated galvanized tube 4’-0” long.

METHOD OF MEASUREMENT

Method of measurement shall be each post and base installed in soil.

BASIS OF PAYMENT

The unit price bid for each post shall include the cost of the post, base, hardware, other materials, labor and equipment necessary to complete the job to the satisfaction of the engineer.

Payment will be made under:

| Item No. | Item | Pay Unit |
| --- | --- | --- |
| C686.04 | Sign Post (12’) | EA |